## Slide 1: AI System Fundamentals & Heterogeneous Computing
Guojie Luo
2026/8/7
Hardware and Software Fundamentals of Intelligent Computing Systems

## Slide 2
Communication Primitives
Communication Topology Optimization

## Slide 3: Scaling Law of LLMs
Model performance improves predictably as a power-law function of compute, data size, and parameter count.

## Slide 4: AI computing systems are also scaling
Scale-up supernodes are on the rise…
NVL72
NVL576
AMD Helios
Huawei CloudMatrix384

## Slide 5: Mapping LLMs on multiple GPUs/NPUs...
Multi-dimension Parallelisms
Expert Parallelism
Sequence Parallelism

## Slide 6: Communication datapath in the AI systems
Scale-up: NVLINK, HCCS, UnifiedBus
Scale-out: InifiniBand (IB), RoCE
Intra-node GPU communications via NVLINK or PCIe
Inter-node communications via RDMA NIC (IB)

## Slide 7: Collective v.s. Point-to-point communications
Collective operations involve communication among a group of processes rather than just between pairs of processes. e.g., AllReduce, AllGather, Bcast
Point-to-point: Send/Recv (Two-side), Put/Get (One-side)

## Slide 8: Broadcast
Operations: copy an N-element buffer from the root rank (2) to all the ranks (0-3).

## Slide 9: Reduce
Operations: performs reduction on data (for example, sum, min, max) across devices and stores the result in the receive buffer of a specified root rank.

## Slide 10: Gather
Operations: gathers N values from k ranks into an output buffer on the root rank of size k*N.

## Slide 11: Scatter
Operations: distributes a total of N*k values from the root rank to k ranks, each rank receiving N values.

## Slide 12: AllReduce
Operations: performs reductions on data (for example, sum, min, max) across devices and stores the result in the receive buffer of every rank.

## Slide 13: AllGather
Operations: gathers N values from k ranks into an output buffer of size k*N, and distributes that result to all ranks.
  The output is ordered by the rank index.
  This operation is therefore impacted by a different rank to device mapping.

## Slide 14: ReduceScatter
Operations: performs the same operation as Reduce, except that the result is scattered in equal-sized blocks between ranks, each rank getting a chunk of data based on its rank index.
  This operation is therefore impacted by a different rank to device mapping.

## Slide 15: AlltoAll
Operations: each rank provides an input buffer of size N values, where the j-th chunk of N/k values is sent to destination rank j. Each rank receives an output buffer of size N values, where the i-th chunk of N/k values comes from source rank i.

## Slide 16: Take FSDP (PyTorch) as an example
DP, DDP, FSDP: Data Parallelism, Distributed DP, Fully Sharded DP
What is DP: multiple model copies on different devices.

## Slide 17: Take FSDP (PyTorch) as an example
DP, DDP, FSDP: Data Parallelism, Distributed DP, Fully Sharded DP
DDP is recommended: optimized all-reduce (ring-based) + distributed support
DP: reduce op is executed on node 0 (imbalance); DDP: ring-based all-reduce.
DDP: robust multi-process support.

## Slide 18: Take FSDP (PyTorch) as an example
DP, DDP, FSDP: Data Parallelism, Distributed DP, Fully Sharded DP
Before FSDP, we profile the memory utilization during the LLM training.
  Model params account for only a portion of the
  total memory consumption during training.
  We need to consider the optimizer states and
  gradients.
Core Idea: removing redundant data.
ZeRO (Zero Redundancy Optimizer).

## Slide 19: Take FSDP (PyTorch) as an example
DP, DDP, FSDP: Data Parallelism, Distributed DP, Fully Sharded DP
ZeRO with different opt levels:
  ZeRO-1: Shards the optimizer states (Optimizer States Sharding).
  ZeRO-2: Shards both optimizer states and gradients (Optimizer States & Gradients Sharding).
  ZeRO-3: Shards the optimizer states, gradients, and model parameters (Optimizer States & Gradients & Parameters Sharding).
ZeRO3 will introduce the extra communications because of the partitions of model parameters.
K denotes the memory multiplier of the optimizer states

## Slide 20: Take FSDP (PyTorch) as an example
DP, DDP, FSDP: Data Parallelism, Distributed DP, Fully Sharded DP
FSDP: sharding model parameters/gradient/optimizer states for GPU memory reduction (ZeRO3).
All-reduce =
Reduce-scatter + all-gather

## Slide 21: Implementations of collective communication op.s
All-reduce = Reduce-scatter + all-gather
Ring All-reduce
NVIDIA GPU CLOS Topology
HUAWEI NPU Full-mesh Topology
The implementations
highly depends on
the hardware topology

## Slide 22: Topologies in the modern AI systems
GOOGLE TPU Torus Topology
HUAWEI NPU Full-mesh Topology
NVIDIA GPU Clos Topology
Dragonfly Topology

## Slide 23: Take AllReduce as an example
Start from a naive implementation with root rank = 0.
  Data transfer volume: 2 * (N-1) * K
There are three disadvantages
  The bandwidth and computation of Rank 0 become bottleneck.
  There are many idle resources during the allreduce (Rank 1 – N-1).
  Poor scalability and lacks the consideration of topology.
How can we improve it?
  Scatter the data transfer and computation workload to all of the ranks.
Solutions:
  Tree-based, ring-based, halving-doubling, etc.

## Slide 24: Take AllReduce as an example
Tree-based AllReduce Algorithm
  Build a hierarchical relation with the root of tree (Rank 0).
  Stage 1: Bottom-up Reduce
  Stage 2: Top-down Broadcast
0
1
2
3
4
5
6
7
0+1
1
2+3
3
4+5
5
6+7
7
Rank 0
Rank 7
S1 Reduce
0+1+2+3
1
2+3
3
4+5+6+7
5
6+7
7
SUM(0,7)
1
2+3
3
4+5+6+7
5
6+7
7

## Slide 25: Take AllReduce as an example
Tree-based AllReduce Algorithm
  Build a hierarchical relation with the root of tree (Rank 0).
  Stage 1: Bottom-up Reduce
  Stage 2: Top-down Broadcast
1
2
3
4
5
6
7
Rank 0
Rank 7
S2 Broadcast
SUM(0,7)
SUM(0,7)
1
2
3
5
6
7
SUM(0,7)
SUM(0,7)
1
SUM(0,7)
3
5
SUM(0,7)
7
SUM(0,7)
SUM(0,7)
SUM(0,7)
SUM(0,7)
SUM(0,7)
SUM(0,7)
SUM(0,7)
SUM(0,7)
SUM(0,7)

## Slide 26: Take AllReduce as an example
Tree-based AllReduce Algorithm
  Build a hierarchical relation with the root of tree (Rank 0).
  Stage 1: Bottom-up Reduce
  Stage 2: Top-down Broadcast
Advantages
  Parallel data transfer and reduce operations.
  Logarithmic complexity (the naive version has linear complexity).
  It excels with small data sizes because of the low latency.
Disadvantages
  It still has idle computing and bandwidth resources.
Further Opt: Double Binary Tree (NCCL)

## Slide 27: Double Binary Tree-based Allreduce
Observation
  in a binary tree: internal/leaves ≈ 50-/50+
Double binary tree
  no rank is internal on both trees
  all ranks have both two parents and two children except for the root
  full bandwidth and logarithmic latency
  good for small and medium size messages

## Slide 28: Take AllReduce as an example
Ring-based AllReduce Algorithm
  Stage 1: Iterative Reduce
  Stage 2: Iterative Gather

## Slide 29: Take AllReduce as an example
Ring-based AllReduce Algorithm
  Stage 1: Iterative Reduce with N-1 steps
  Stage 2: Iterative Gather with N-1 steps
Split the data with N partitions

## Slide 30: Take AllReduce as an example
Ring-based AllReduce Algorithm
  Stage 1: Iterative Reduce with N-1 steps
  Stage 2: Iterative Gather with N-1 steps

## Slide 31: Take AllReduce as an example
Ring-based AllReduce Algorithm
  Stage 1: Iterative Reduce with N-1 steps
  Stage 2: Iterative Gather with N-1 steps

## Slide 32: Take AllReduce as an example
Ring-based AllReduce Algorithm
  Stage 1: Iterative Reduce with N-1 steps
  Stage 2: Iterative Gather with N-1 steps

## Slide 33: Take AllReduce as an example
Ring-based AllReduce Algorithm
  Stage 1: Iterative Reduce with N-1 steps
  Stage 2: Iterative Gather with N-1 steps

## Slide 34: Take AllReduce as an example
Ring-based AllReduce Algorithm
  Stage 1: Iterative Reduce with N-1 steps
  Stage 2: Iterative Gather with N-1 steps

## Slide 35: Take AllReduce as an example
Ring-based AllReduce Algorithm
  Stage 1: Iterative Reduce with N-1 steps
  Stage 2: Iterative Gather with N-1 steps
Quantitative Analysis
  Data Transfer Volume: 2 * (N-1) * K / N
  Overall Time: 2 * (N-1) * alpha + 2 * (N-1) * K / N / beta
  Tree-based AllReduce Time : 2 * log(N) * (alpha + K / beta)
  alpha: latency; beta: bandwidth
Advantages: Optimal bandwidth utilization

## Slide 36: Take AllReduce as an example
Ring-based AllReduce Algorithm
  Stage 1: Iterative Reduce with N-1 steps
  Stage 2: Iterative Gather with N-1 steps
Quantitative Analysis
  Data Transfer Volume: 2 * (N-1) * K / N
  Overall Time: 2 * (N-1) * alpha + 2 * (N-1) * K / N / beta
  Tree-based AllReduce Time : 2 * log(N) * (alpha + K / beta)
  alpha: latency; beta: bandwidth
Advantages: Optimal bandwidth utilization

## Slide 37: Take AllReduce as an example
Halving-doubling AllReduce Algorithm
  Stage 1: Recursive halving reduce
  Stage 2: Recursive doubling gather

## Slide 38: Take AllReduce as an example
Comparisons among ring-based, tree-based, and halving-doubling Allreduce algorithms.
Modern CCLs can select an efficient strategy according to the topology and the communication domain.
Algorithm | Steps (Complexity) | Latency | Bandwidth Efficiency | Ideal Data Size
Ring-based | O(N) | High | Optimal | Large Data (> 64MB)
Tree-based | O(log N) | Lowest | Moderate | Small-Medium (< 16MB)
Halving-Doubling | O(log N) | Low | Moderate | Very Small (< 1MB)
Notes: https://zhuanlan.zhihu.com/p/1976385706453652306

## Slide 39: Protocol design matters
Take NCCL as an example.

## Slide 40: Besides, the protocol designs are also important
Take NCCL as an example.
Notes: https://zhuanlan.zhihu.com/p/1976385706453652306

## Slide 41: Broadcast (a.k.a., One-to-All Boardcast)
Among a group of processing elements (nodes), a designated root node has a data item to be communicated (copied) to all other nodes.
  All nodes are assumed to explicitly take part in the broadcast operation.
  It is generally assumed that before its execution all nodes know the index of the designated root node as well as the the amount n of data to be broadcast.
  The data item x may be either a single, atomic unit or divisible into smaller, disjoint pieces.
    The latter can be exploited algorithmically when n is large.

## Slide 42: Broadcast: Assumptions
Assumptions in the following analysis (for this lecture ONLY)
  All nodes can communicate through a communication network.
  Individual nodes perform communication operations that send and/or receive individual messages.
  Communication is through a single port
    (such that a node can be involved in at most one communication operation at a time)
    Such an operation can be either a send to or a receive from another node (unidirectional communication),
    a combined send to and receive from another node (bidirectional, telephone like communication), or
    a send to and receive from two possibly different nodes (simultaneous sendreceive, fully bidirectional communication).
  The communication medium is homogeneous and fully connected
  A first approximation for the transferring time between two nodes: α + nβ
    n is the message size
    α is the start-up cost (latency)
    β is the cost per item transfered (inverse of the bandwidth)

## Slide 43: Broadcast: Two Lower Bounds
Two lower bounds
  for the term:
    a round: during which each node can send at most one message and receive at most one message.
    In each round, the number of nodes that know message x can at most double.
    Thus, a minimum of rounds are needed to broadcast the message.
    Each round costs at least .
  for the term:
    If then the message must leave the root node, requiring a time of at least .
Notes
  When assumptions about the communication system change, these lower bounds change as well.
  Lower bounds for mesh and torus networks, hypercubes, and many other topologies are known[WGe95].
  Determining the minimum broadcast time in an arbitrary, given graph is NP-hard [JaM95]

## Slide 44: Broadcast: Tree-based Algorithms
Notes: A binomial tree of order k is recursively defined as follows.
* A binomial tree of order 0 is a single node.
* A binomial tree of order k>0 consists of a root node and k children, where the i th child of the root is the root of a binomial tree of order i, 0<=i<=k-1.

## Slide 45: Broadcast: The “MST” Algorithm
The so-called* Minimum Spanning Tree (MST) algorithm
  Partition the set of nodes into two roughly equalsized subsets.
  Send x from the root to a node in the subset that does not include the root.
    The receiving node will become a local root in that subset.
  Recursively broadcast x from the (local) root nodes in the two subsets.
The total cost of the MST algorithm:
  It achieves the lower bound for the α term
  but not for the β term for which it is a logarithmic factor off from the lower bound.
The MST algorithm constructs a binomial spanning tree over the set of nodes
  Figure (d) in the previous slide
Notes: [SuB77] Herbert Sullivan and T R Bashkow. “A large scale, homogeneous, fully distributed parallel machine,” ISCA 1977.

## Slide 46: Broadcast: Pipelining
For large n, pipelining improves the broadcast cost
  the message is split into k blocks of size n/k each
In the “path” boradcast tree:
  The first piece from node 0 takes p-1 rounds to reach node p-1
  an additional k-1 rounds for the remaining k-1 pieces
  total time cost = ≥
    with optimal number of blocks
Pipelining can be applied on fixed degree trees
  Binary tree: best-effort time cost =
  Fibonacci tree: best-effort time cost = where
Pipelining is not helpful on nonconstant degrees trees (e.g., binomial tree and star graph)

## Slide 47: Broadcast: the Third Lower Bound
The third lower bound on the number of rounds:
  first piece rounds plus k-1 additional rounds
  total time cost = ≥
    with optimal number of blocks

## Slide 48: Broadcast: Simultaneous Trees
optimal k - 1 + log2p rounds of pipelining
  when the message is split into k blocks
p=2d nodes in a d-dimensional hypercube
  node id: i ∈ { 0, 1, ..., 2d-1 } with ij as the j-th bit
d edge-disjoint spanning binomial trees (ESBT)
  all trees are rooted at node 0
  the j-th tree has 2d-1-1 leaves with ij=0
  the j-th tree broadcasts blocks j, j+d, j+2d, ...
Leaves in tree j = t%d receive block t-d in round t
  block -d, 1-d, ..., -1, 0, 1, ..., k-1
BitDistancei[j]: distance to the next 1 to the left of ij
  BitDistance0[k] ≡ k for 0 < k ≤ d
Notes: a hypercube has d 2d (bidirectional) edges
d ESBTs have d (2d-1) edges in total
each "for" loop contains d rounds, except the first loop takes k%d rounds
t-d: 当前的block号

## Slide 49: Further Readings
van de Geijn, R., Träff, J. (2011). Collective Communication. In: Padua, D. (eds) Encyclopedia of Parallel Computing. Springer, Boston, MA.
Träff, J.L., van de Geijn, R.A. (2011). Broadcast. In: Padua, D. (eds) Encyclopedia of Parallel Computing. Springer, Boston, MA.
Träffe, J.L., van de Geijn, R.A. (2011). Allgather. In: Padua, D. (eds) Encyclopedia of Parallel Computing. Springer, Boston, MA.
Träff, J.L., vande Geijn, R.A. (2011). All-to-All. In: Padua, D. (eds) Encyclopedia of Parallel Computing. Springer, Boston, MA.